## Slide 1
MASTER'S THESIS · PROGRESS MEETING · MAY 5, 2026
Whole-Body Control
for Humanoid Robots
Literature Review · Research Positioning · Work Plan
RESEARCH QUESTION
Can a two-layer MPC + QP-WBC framework on TALOS be rigorously evaluated
through a reproducible, scenario-based protocol in MuJoCo simulation?
David · Thesis Deadline: August 26, 2026

## Slide 2
2. Proposed System Architecture
WBC Humanoid Thesis | May 5, 2026
Task references
State estimate
CENTROIDAL MPC
Crocoddyl · ~100 Hz
Centroidal dynamics / DDP solver
CoM trajectory · contact force refs
QP-WBC
Pinocchio + TSID · ~1 kHz
Task hierarchy + contact QP
Joint torques (N·m)
TALOS · MuJoCo
32-DoF humanoid · rigid contacts
state
feedback
Locked Design Decisions
ROBOT
TALOS — 32-DoF torque-controlled; Pinocchio URDF
SIMULATOR
MuJoCo — rigid contacts, <1 ms step, free licence
ARCHITECTURE
MPC + QP-WBC hierarchy — proven on Atlas, HRP-4
NOVELTY
Reproducible eval protocol: S1–S5 + standard metrics

## Slide 3
3. Three Paradigms in Whole-Body Control
WBC Humanoid Thesis | May 5, 2026
QP / Task-Priority
Khatib (1987) — Operational Space
Sentis & Khatib (2005) — Null-space WBC
Saab et al. (2013) — Dynamic WBC contacts
Escande et al. (2014) — HQP (canonical)
Del Prete (2016) — TSID framework
Dominant in industry (Atlas, HRP-4)
MPC-Based
Wensing & Orin (2013) — Conic task-space
Koolen et al. (2016) — Momentum, Atlas
Sleiman et al. (2021) — Loco-manipulation MPC
Romualdi et al. (2023) — Online centroidal NMPC
Wensing et al. (2024) — Optimization survey
Real-time feasibility still challenging
Learning-Based
Radosavovic et al. (2024) — Real humanoid RL
ASAP (2025) — Residual WBC sim-to-real
HumanoidBench (2024) — Eval benchmark
PolySim (2025) — Multi-sim randomization
LeCleach et al. (2024) — Contact-implicit MPC
Rapidly closing gap with model-based

## Slide 4
4. Where the Field Converges
WBC Humanoid Thesis | May 5, 2026
01
Centroidal Dynamics Are Sufficient for Planning
Orin et al. (2013) establish centroidal momentum as the minimal planning abstraction. All major WBC frameworks — Atlas, NMPC, TSID — exploit this formulation. Planning in full-body space adds cost with no empirical benefit at control rates.
02
HQP Is the Dominant Execution Paradigm
Escande et al. (2014) canonicalize fast HQP for humanoid motion. Del Prete (2016) operationalizes it in TSID. Strict priority handling + inequality constraints make QP-WBC the industry-standard execution layer.
03
Contact Stability Requires QP-Based Wrench Distribution
Despite differing positions on compliance (Righetti vs Saab 2013), the community converges on QP optimization for contact force distribution. Friction cone linearization remains the pragmatic standard for real-time control.
04
Sim-to-Real Gap Persists for Contact-Rich Tasks
PolySim (2025) and ASAP (2025) address domain randomization — validated on locomotion. Multi-contact manipulation in simulation lacks standardized protocols, leaving real-world deployment largely trial-and-error.

## Slide 5
5. Three Critical Research Gaps
WBC Humanoid Thesis | May 5, 2026
GAP 1
Reproducibility Crisis in WBC Evaluation
No standardized benchmark exists for comparing WBC controllers across simulators. Papers report different metrics (CoM error, ZMP margin, energy), different scenarios, and different perturbation magnitudes — making cross-paper comparison impossible.
→ Our contribution directly addresses this gap with protocol S1–S5
GAP 2
Architecture Fragmentation: Model-Based vs Learning
Model-based (TSID, Crocoddyl) and learning-based (ASAP, Radosavovic 2024) controllers coexist with no head-to-head comparison under identical conditions. Hybrid MPC + QP architectures remain underexplored on standard platforms.
→ Our two-layer architecture bridges MPC and QP in one reproducible framework
GAP 3
Contact-Rich Scenarios Lack Systematic Benchmarking
MuJoCo-based validation dominates for flat-ground locomotion. Stair climbing and whole-body manipulation under contact forces are rarely benchmarked in simulation before real-world deployment.
→ Scenarios S4–S5 explicitly target contact-rich loco-manipulation

## Slide 6
6. Research Positioning — Our Contribution vs SOTA
WBC Humanoid Thesis | May 5, 2026
Criterion
Crocoddyl
TSID / SoT
RL (ASAP)
Our Approach
Architecture
DDP / MPC
Task-Priority QP
End-to-end RL
2-layer MPC + QP
Robot Platform
ANYmal, HRP
HRP-4, iCub
Digit, H1, G1
TALOS
Simulator
Crocoddyl env
Gazebo / ROS
IsaacGym/MuJoCo
MuJoCo
Eval Protocol
Ad-hoc
Ad-hoc
Task reward
Standardized S1–S5
Open-source
✓
✓
Partial
Targeted ✓
Sim-to-real
Partial
Validated
Strong
Simulation focus
← This thesis

## Slide 7
7. Proposed Approach & Evaluation Protocol
WBC Humanoid Thesis | May 5, 2026
Control Architecture
Task
References
MPC
~100 Hz
CoM refs
contact forces
QP-WBC
~1 kHz
Joint
torques
TALOS
MuJoCo
state feedback
Pinocchio (dynamics) · Crocoddyl (MPC) · TSID (WBC) · MuJoCo (sim)
Contact model
Rigid unilateral constraints · friction cone QP · wrench distribution
State estimation
Perfect observation in simulation · realistic noise planned for S3–S5
Evaluation Scenarios (S1–S5)
Simple
Complex
← Complexity →
S1
Static Balance
Postural stability, joint limit compliance
S2
Walking — Flat Ground
Forward gait, CoM height regulation
S3
Push Recovery
External force rejection (10–50 N impulse)
S4
Stair Climbing
Contact-rich locomotion, foot placement
S5
Object Manipulation
Whole-body loco-manipulation under load
Metrics: CoM deviation · ZMP margin · Joint torque RMS · Recovery time · Energy / step

## Slide 8
8. Work Plan — May to August 2026
May 5
Jun 1
Jul 1
Aug 1
Aug 26
Deadline
COMPLETED (pre-meeting)
Ch.2 State of the Art
✓ DONE — Literature review + bib audit
Overleaf zip rebuild
✓ DONE — 7 fake refs removed
UPCOMING WORK
Ch.1 Introduction
Motivation · RQ · scope
Ch.3 Methodology
QP-WBC formulation
GitHub push + bib fixes
Sim Setup (TALOS+MuJoCo)
URDF · Pinocchio · WBC stack
S1–S3 Experiments
Balance · Walk · Push recovery
S4–S5 Experiments
Stairs · Manipulation
Ch.4–5 Writing
Simulation + Results
Ch.6–7 Discussion
Analysis · Conclusion
Final Review + Buffer
WBC Humanoid Thesis | May 5, 2026