## Slide 1
MASTER'S THESIS · PROGRESS MEETING · 05 MAY 2026
Whole-Body Control for Humanoid Robots.
A simulation-first foundation.
CANDIDATE
David Mazé
SUPERVISION
DR Gilbert Tang
Pr Phil Webb
DEPARTMENT
Cranfield University
Robotics MSc
SUBMISSION
26 August 2026
T − 16 weeks
Original title — "Development & Simulation of a Whole-Body Control Framework for a Humanoid Robot"
FIG. 0 — TALOS · 32 DOF
MUJOCO · 1 KHZ
COVER
05 · MAY · 2026
01/18

## Slide 2
01 · PROGRAMMATIC CONTEXT
·
5-YEAR STRATEGIC PLAN
The 5-year humanoid robotics program.
This thesis is thefirst academic output of a long-term institutional program — so generality and reproducibility are the primary design constraints.
▼ WE ARE HERE
2026
Year 1
Theoretical foundations
Literature, control formulation, simulation framework, evaluation protocol.
2027
Year 2
Simulation maturity
Extended scenarios, sim-to-real preparation, second-generation control.
2028
Year 3
Hardware integration
Acquisition of TALOS-class hardware, first physical experiments.
2029
Year 4
First prototypes
Closed-loop control on real hardware, on-board perception, manipulation.
2030
Year 5
Autonomous humanoid
Integrated whole-body autonomy in unstructured environments.
No physical hardware exists yet. Every decision made now must beforward-compatible — we are building the foundations the next researchers will inherit.
SECTION 1 · CONTEXT
05 · MAY · 2026
02/18

## Slide 3
02 · POSITION IN THE PROGRAM
·
THE BRIDGE LAYER
Where this thesis fits.
L3 · YEAR 5
Autonomous humanoid system
Integrated cognition, perception, manipulation.
L2 · YEAR 3–4
Hardware integration
Real TALOS · sim-to-real transfer · on-board perception.
L1 · YEAR 1 · THIS THESIS
Simulation framework + evaluation protocol
MPC + QP-WBC on TALOS in MuJoCo. Reproducible S1–S5 protocol. Open-source, modular, documented.
MANDATORY FRAMEWORK PROPERTIES
01
Modular
Components swap as the hardware program evolves — physics engine, dynamics library, even the planner itself.
02
Reproducible
Every result reruns from a single command. Seeds, configs and metrics are version-controlled alongside the code.
03
Well-documented
Next researchers extend the framework — they do not restart it. README, tutorials, and inline derivations.
Without this floor, hardware work has nothing to build on.
SECTION 1 · CONTEXT
05 · MAY · 2026
03/18

## Slide 4
03 · REFINING THE PROBLEM
·
FROM TOPIC TO QUESTION
From broad topic to a precise research question.
ORIGINAL TOPIC
"Development & simulation of a whole-body control model for a humanoid robot."
WHY THIS IS NOT ENOUGH
×
Which whole-body control approach? (dozens exist)
×
Which humanoid? Which simulator?
×
What does success look like? How is it measured?
×
No evaluation criterion → no way to know if we succeeded.
REFINED RESEARCH QUESTION
Can atwo-layer MPC + QP-WBC framework, implemented on TALOS in MuJoCo , be rigorously evaluated through a reproducible scenario-based protocol — and serve as a reusable simulation foundation for future hardware integration?
ARCHITECTURE
MPC + QP-WBC two-layer hierarchy
PLATFORM
TALOS robot · MuJoCo simulator
EVALUATION
Reproducible S1–S5 protocol
LONG-TERM GOAL
Reusable foundation for the program
SECTION 2 · PROBLEM
05 · MAY · 2026
04/18

## Slide 5
04 · STRATEGY
·
A DESIGN CHOICE, NOT A LIMITATION
Why "simulation-first" is the right strategy.
SIMULATION ENVIRONMENT
COST
Negligible
ITERATION
Minutes
REPEATABILITY
1.000
DAMAGE RISK
None
Rapid iteration, parameter sweeps, and reproducible experiments without physical risk.
REAL HARDWARE (YEAR 3+)
COST
€ 500k+
ITERATION
Days
REPEATABILITY
Drift
DAMAGE RISK
High
Expensive, unforgiving, and unavailable during early-stage research.
SIM-TO-REAL TRANSFER
A solved research problem for locomotion.
Domain randomization & contact-model tuning bridge the gap. By design, only the hardware-interface layer changes when physical TALOS arrives — the MPC + QP-WBC stack is identical in sim and on real hardware.
SECTION 2 · PROBLEM
05 · MAY · 2026
05/18

## Slide 6
05 · STATE OF THE ART
·
40 YEARS · 3 PARADIGMS
Forty years of whole-body control.
QP / Task-Priority
MPC-Based
Learning-Based
1985
1995
2005
2015
2025
1987→
Khatib
1987
Sentis & Khatib
2005
Escande
2014
Del Prete
2016
2013→
Wensing & Orin
2013
Koolen
2016
Sleiman
2021
Romualdi
2023
2022→
Radosavovic
2024
ASAP
2025
PolySim
2025
2026 ▼
Each generation solves part of the problem — none subsumes the others. Our framework deliberately sits in the most-validated branch (model-based) while staying compatible with the newest one (learning-based).
SECTION 3 · LITERATURE
05 · MAY · 2026
06/18

## Slide 7
06 · WHAT THE FIELD AGREES ON
·
FOUR INVARIANTS
Four points of consensus.
Across three paradigms and four decades, the community has converged on these — they are the non-negotiables our framework must respect.
01· CONSENSUS
ORIN ET AL. 2013
Centroidal dynamics suffice for planning.
A 32-DoF body abstracts to a 6-DoF centroidal model for trajectory planning. Every major framework does this; full-body planning adds compute with no empirical benefit at control rates.
02· CONSENSUS
ESCANDE 2014 · DEL PRETE 2016
Hierarchical QP is the dominant execution paradigm.
Strict task priority — "don't fall" beats "track the arm" — plus inequality constraints (joint limits, friction cones) make QP-WBC the industry-standard execution layer.
03· CONSENSUS
RIGHETTI 2013 · SAAB 2013
Contact stability requires QP wrench distribution.
Whether the contact model is rigid or compliant, all serious WBC systems solve a QP to distribute forces across contacts and enforce friction-cone constraints.
04· CONSENSUS
ASAP 2025 · POLYSIM 2025
The sim-to-real gap persists for contact-rich tasks.
Domain randomization handles flat-ground walking. Stair climbing and sustained-contact manipulation remain unsolved in simulation-to-hardware transfer.
SECTION 3 · LITERATURE
05 · MAY · 2026
07/18

## Slide 8
07 · THE METHODOLOGICAL GAP
·
THE REPRODUCIBILITY CRISIS
The reproducibility problem in WBC.
You cannot compare papers because everyone uses a different robot, simulator, scenario and metric. This is the field's biggest unsolved methodologicalproblem.
CURRENT STATE OF WBC EVALUATION
PAPER
ROBOT
SIMULATOR
SCENARIO
METRIC
Koolen 2016
Atlas
custom
Balance
ZMP margin
Sleiman 2021
ANYmal
RaiSim
Walking
CoT
Romualdi 2023
iCub
Gazebo
Push recovery
Recovery time
ASAP 2025
Unitree H1
IsaacGym
Locomotion
RL reward
PolySim 2025
?
multi
?
?
?= not reported · units inconsistent · scenarios non-standardized
0
papers using the same robot + sim + scenario + metric set
5
different simulators across these 5 papers
∅
cross-paper benchmarks · comparison is impossible
Researchers can't tell if controller A isbetter than B — or justtested on an easier scenario.
SECTION 3 · LITERATURE
05 · MAY · 2026
08/18

## Slide 9
DECISION 1 OF 4
·
THE ROBOT
TALOS — the only realistic, fully torque-controlled platform.
× REJECTED
Unitree H1/G1
POSITION-CONTROLLED
+
Popular in RL
−
Not torque-controlled
−
Limited dynamics access
× REJECTED
Boston Dynamics Atlas
CLOSED-SOURCE
+
Industry benchmark
−
No public URDF
−
Not reproducible
× REJECTED
Custom simplified
TOY MODEL
+
Quick to build
−
Too abstract
−
Not transferable
✓ CHOSEN
TALOS · PAL Robotics
32 DOF · TORQUE-CONTROLLED
+
Open URDF
+
Pinocchio-compatible
+
Used in WBC literature
+
Likely Year-3 platform
WHY TALOS
Full Pinocchio dynamic model · torque control compatible with QP-WBCand direct RL · community-validated in WBC papers · most likely starting point when university hardware arrives.
32 DOF
PAL ROBOTICS
SECTION 4 · DECISIONS
05 · MAY · 2026
09/18

## Slide 10
DECISION 2 OF 4
·
THE SIMULATOR
MuJoCo — fastest, most accurate, most compatible.
BENCHMARK · NORMALIZED 0–100
Gazebo
35
60
75
Slower than real-time
PyBullet
70
30
80
Unreliable foot contacts
IsaacGym
95
75
60
NVIDIA license
MuJoCo ✓ CHOSEN
100
95
95
all green
SPEED
CONTACT ACCURACY
PYTHON API
MUJOCO VIEWPORT · 1 KHZ
WHY MUJOCO
< 1 ms
step time → enables 1 kHz control loop
2022
open-sourced by DeepMind · no license cost
3/3
Radosavovic · ASAP · HumanoidBench all use it
∂F/∂q
contact forces inspectable per timestep
SECTION 4 · DECISIONS
05 · MAY · 2026
10/18

## Slide 11
DECISION 3 OF 4
·
THE CONTROL ARCHITECTURE
A two-layer hierarchy: theoretically grounded, real-time capable.
TWO-LAYER CONTROL ARCHITECTURE
INPUT
Task references + state estimate
GOALS · Q̂, Q̇̂
LAYER 1 · 100 HZ
Centroidal MPC
Crocoddyl
COM TRAJECTORY · CONTACT FORCE REFS
LAYER 2 · 1 KHZ
QP-WBC
Pinocchio + TSID
Τ — JOINT TORQUES (N·M)
PLANT
TALOS in MuJoCo
STATE FEEDBACK
THREE OPTIONS · ONE VIABLE
×
Pure QP-WBC
Reactive only · no predictive contact planning
×
Pure MPC
Too slow at 1 kHz · joint limits hard
×
End-to-end RL
Data-hungry · black-box · not generalizable
WHY TWO LAYERS
MPC handles long-horizon contact prediction; QP-WBC enforces strict task hierarchy and joint limits in real time. Both are model-based — interpretable, debuggable, transferable to hardware.
Validated on Atlas (Koolen ’16) · HRP-4 (Caron ’19) · ANYmal (Sleiman ’21).
SECTION 4 · DECISIONS
05 · MAY · 2026
11/18

## Slide 12
DECISION 4 OF 4
·
THE CONTRIBUTION
Our novelty is not a new algorithm — it's a reproducible protocol.
STATUS QUO
Every paper in its own bubble. No shared protocol. No comparison.
WITH THIS THESIS
All experiments share S1–S5. Direct, fair comparison becomes possible.
S1–S5 EVALUATION PROTOCOL
S1
Static balance
Postural stability, joint limits
S2
Flat-ground walking
Gait, CoM-height regulation
S3
Push recovery
Force rejection (10–50 N impulse)
S4
Stair climbing
Contact-rich locomotion
S5
Loco-manipulation
Walking + arm payload
STANDARDIZED METRICS
CoM deviation · ZMP margin · Joint torque RMS · Recovery time · Energy per step
Any future team adding a new algorithm runs S1–S5 and immediately knows whether they improved or regressed. This baseline does not exist today.
SECTION 4 · DECISIONS
05 · MAY · 2026
12/18

## Slide 13
08 · OPEN PROBLEMS
·
THREE GAPS · THREE ANSWERS
Three gaps we close.
GAP 1
Reproducibility crisis
PROBLEM
No two WBC papers share scenario, metric or platform — cross-paper comparison is impossible. The field cannot tell whether controllers improve over time.
OUR ANSWER
S1–S5 standardized protocol with fixed metrics. Future papers compare against our baseline.
GAP 2
Architecture fragmentation
PROBLEM
Model-based (TSID, Crocoddyl) and learning-based (ASAP, Radosavovic) controllers are evaluated in isolation, with no common ground.
OUR ANSWER
Two-layer MPC + QP-WBC on TALOS in MuJoCo — the same setup RL researchers use. Direct comparison becomes possible.
GAP 3
Contact-rich scenarios underexplored
PROBLEM
90 % of WBC validation is flat-ground locomotion. Stair climbing and manipulation in simulation before hardware deployment are systematically avoided.
OUR ANSWER
S4 and S5 explicitly force the controller into contact-rich regimes — with standardized metrics for them.
SECTION 5 · GAPS
05 · MAY · 2026
13/18

## Slide 14
09 · BEYOND THIS THESIS
·
A ROADMAP FOR FUTURE RESEARCHERS
What we leave open — by design.
We are not trying to solve everything. We build the floor — here is what comes next.
DONE
L1
Simulation framework + S1–S5 protocol
—
Two-layer MPC + QP-WBC on TALOS
—
MuJoCo environment, reproducible
—
Open-source, documented, modular
NEXT · YEAR 3
L2
Hardware integration
—
Replace MuJoCo state estimator with IMU + encoder fusion
—
Tune contact model to physical TALOS foot compliance
—
Run S1–S3 on real hardware, report sim-to-real gap
—
Extend Crocoddyl planner with learned residuals (test on S4–S5)
—
Vision-based perception for unstructured terrain (S4 ext.)
LATER · YEAR 4–5
L3
Benchmark + autonomy extensions
—
S6 — dynamic obstacle avoidance
—
S7 — collaborative human + humanoid task
—
Dual-arm manipulation with external object models
—
Battery-life energy metrics on hardware
—
End-to-end autonomous task execution
Every component is open-source, documented and modular. Future researchersextend— they do notrestart.
SECTION 5 · GAPS
05 · MAY · 2026
14/18

## Slide 15
10 · WHAT HAS SHIPPED
·
APR 13 → MAY 5
Three weeks · the theoretical foundation is complete.
TASK
START
END
✓
Literature review · Ch. 2 State of the Art, Bibliography
Apr 13
Apr 28
✓
Dedicated Github repository created
Apr 23
Apr 28
✓
Architecture decisions
Apr 28
Apr 30
✓
LaTeX+ thesis structure
Apr 28
Apr 30
SECTION 6 · PLAN
05 · MAY · 2026
15/18

## Slide 16
11 · ROADMAP
·
16 WEEKS · 9 WORK PACKAGES · 4 MILESTONES
Roadmap to 26 August.
WRITING
SIMULATION
EXPERIMENTS
REVIEW
ADMIN
MAY 5
JUN 1
JUL 1
AUG 1
AUG 26
WRITING
Ch. 1 · Introduction
WRITING
Ch. 3 · Methodology (QP-WBC formulation)
ADMIN
GitHub management
SIMULATION
Environment setup · TALOS + MuJoCo + Pinocchio
EXPERIMENTS
S1–S3 · Balance, Walking, Push Recovery
EXPERIMENTS
S4–S5 · Stair Climbing, Manipulation
WRITING
Ch. 4–5 · Simulation & Results
WRITING
Ch. 6–7 · Discussion & Conclusion
REVIEW
Final review · proofreading · buffer
MILESTONES
JUN 15 · SIM ENV
JUL 10 · S1–S3 DONE
JUL 25 · ALL SCENARIOS
AUG 14 · FULL DRAFT
SECTION 6 · PLAN
05 · MAY · 2026
16/18

## Slide 17
12 · CLOSING
·
WHAT WE NEED FROM YOU
Three asks before implementation begins.
Implementation begins 20 May. Locking these three points now keeps the next 16 weeks on track.
01
FRAMING
Research-question validation
Is the refined RQ — "reproducible scenario-based evaluation protocol as a reusable foundation" — the right angle for the program's Year-1 output?
02
SCOPE
S1–S5 scenario scope
Are the five scenarios realistic for a single master's thesis? Should S5 (loco-manipulation) be de-risked to an optional extension?
03
OUTPUT
Deliverable expectations
Are the expected deliverables — framework + protocol + documented code + thesis — aligned with what the program needs for Year-3 hardware integration?
CLOSING
05 · MAY · 2026
17/18

## Slide 18
13 · RECAP
·
ONE SLIDE TO LEAVE ON SCREEN
Five takeaways.
01
CONTEXT
First thesis in a 5-year humanoid robotics program
Generality and reproducibility are the primary constraints — not optional refinements.
02
PROBLEM
Reproducible simulation-first WBC framework for TALOS
A foundation that future hardware teams can transplant without re-deriving the stack.
03
ARCHITECTURE
Two-layer MPC (Crocoddyl) + QP-WBC (TSID) on MuJoCo
Open-source, modular, theoretically grounded — and validated on Atlas, HRP-4, ANYmal.
04
NOVELTY
S1–S5 standardized evaluation protocol
The missing baseline in WBC research — fixed scenarios, fixed metrics, comparable results.
05
TIMELINE
Theory complete · implementation 20 May · submission 26 Aug
4/4 planned tasks delivered on schedule. 16 weeks remain. 4 milestones tracked.
Thank you.
SUBMISSION · 26 AUG 2026
SUMMARY
05 · MAY · 2026
18/18